Drop-off Locker
User Manual and Design Schematic
Index
About Drop-off Locker………….	1
General use guide……………….	1
Administrator guide…………….	2
Troubleshoot and repair guide….	3
Circuit Design…………………..	4
Source Code…………………….	5
Fabrication Notes……………….	12
Upgrade Notes………………….	13
Contact Info…………………….	14

k

#define LED_D 13 //bottom
#define LED_C 12
#define LED_B 11
#define LED_A 10 //top
#define B_EN_D 9
#define B_EN_C 8 //back button
#define B_EN_B 7 //front button
#define B_EN_A 6 //priority set(control panel)

#define LCK_D 5 //bottom
#define LCK_C 4
#define LCK_B 3
#define LCK_A 2 //top
#define B_IN_D 3
#define B_IN_C 2
#define B_IN_B 1
#define B_IN_A 0
#define LOCKED 0
#define UNLOCKED 1
#define TAKEN 1
#define OPEN 0
#define LOOPS_TO_HR 36000
#define WATHCHDOG_LIMIT 50 //5 seconds limit

#define ACTIVE_LOW_RELAY

struct QuadState
{
  bool s[4];
};
struct QuadCount
{
  int c[4];
};

//lock access (TAKEN/OPEN)
QuadState gLockLed;
//current state of lock(LOCKED/UNLOCKED)
QuadState gLock;
//button state (per poll per set)
QuadState gBtn;

//avoid holding solenoid lock if button jams in
QuadState gWatchDogHit;
QuadCount gWatchDogCnt;

//how many hours till locking
unsigned short gLkTmr;
//no available pins to allow for interupt based timer.
//keep track of hours by counting loops
unsigned int gHrTmr;
//perserve last state of button/switch to trigger event on changed state
bool gLastTToggle; //for changing time
bool gLastLToggle; //for locking/unlocking all in admin mode
bool gLastAMode; //check if admin mode was just entered

//TODO: add watchdog timer for held lock buttons

void setup()
{
  // Initialize the digital pin as an output.
  for(int i = 6; i < 14; i++)
  {
    pinMode(i, OUTPUT);
    digitalWrite(i, 0);
  }
  for(int i = 0; i < 4; i++)
  {
    pinMode(i+LCK_A, OUTPUT);
#ifdef ACTIVE_LOW_RELAY
    digitalWrite(i+LCK_A, 1);
#else
    digitalWrite(i+LCK_A, 0);
#endif
  }

  Serial.begin(9600);
  Serial.println("LOCKER STARTING UP....");

/* Debug code
  //startup debug blink
  for(int d = 0; d < 4; d++)
  {
    for(int t = 0; t < 4; t++)
    {
      delay(500);
      for(int i = LED_A; i <= LED_D; i++) { digitalWrite(i, LOCKED); }
      delay(500);
      debugBtnShow(d);
      //for(int i = LED_A; i <= LED_D; i++) { digitalWrite(i, UNLOCKED); }
    }
  }
*/

  //set default values
  for(int i = 0; i < 4; i++)
  {
    gLock.s[i] = LOCKED;
    gLockLed.s[i] = TAKEN;
  }

  gLkTmr = 4;

  gLastTToggle = false;
  gLastLToggle = false;
  gLastAMode = false;

  gHrTmr = LOOPS_TO_HR;

  //start watchdog with clean slate (no open locks)
  watchdogTick();

  showLockState();
  Serial.println("SYSTEM INITIALIZED....");
}

void loop()
{
  bool adminMode = false;
  bool activeTimer = false;
  bool toggleLock = false;

//button routines=================================================================
  //admin setup-------------------------------------------------------------------
  delay(25);
  readBtn(0);
  adminMode = gBtn.s[0];
  activeTimer = gBtn.s[1];
  toggleLock = gBtn.s[2];

  if(activeTimer && adminMode && (gLkTmr == 0))
  {
    gLkTmr = 4;
  }
  else if(!activeTimer)
  {
    gLkTmr = 0;
  }

  if((adminMode) && (toggleLock != gLastLToggle) && gLastAMode)
  {
    setAllState(toggleLock ? TAKEN : OPEN);
  }
  gLastLToggle = toggleLock;
  gLastAMode = adminMode;

  //front button------------------------------------------------------------------
  delay(25);
  readBtn(1);
  if(adminMode)
  {
    for(int i = 0; i < 4; i++)
    {
      gLock.s[i] = gBtn.s[i];
    }
  }
  else
  {
    for(int i = 0; i < 4; i++)
    {
      gLock.s[i] = gBtn.s[i] && (gLockLed.s[i] == OPEN);
    }
  }

  //rear button-------------------------------------------------------------------
  delay(25);
  readBtn(2);
  for(int i = 0; i < 4; i++)
  {
    if(adminMode) { gLockLed.s[i] &= !gBtn.s[i]; }
    else { gLockLed.s[i] |= gBtn.s[i]; }
  }
  if(adminMode)
  {
    if(activeTimer && !gLastTToggle && gBtn.s[0])
    {
      toggleTimer();
    }
    gLastTToggle = gBtn.s[0];
  }
  else { gLastTToggle = false; }

  //for future improvements/debug ------------------------------------------------
  delay(25);
  readBtn(3);
  //add code as needed

//show results ===================================================================
  //display state
  if(adminMode)
  {
    showTimerState();
  }
  else
  {
    showLockState();
  }

  watchdogTick();
  triggerLock();

  //check for timer event (reaching an hour)
  gHrTmr--;
  if(!gHrTmr)
  {
    hrHit();
  }
}

void watchdogTick()
{
  for(int i = 0; i < 4; i++)
  {
    if(gWatchDogHit.s[i])
    {
      if(!gLock.s[i]) { gWatchDogCnt.c[i] = 0; }
    }
    else
    {
      gWatchDogCnt.c[i] = gLock.s[i] ? gWatchDogCnt.c[i]+1 : 0;
    }

    gWatchDogHit.s[i] = (gWatchDogCnt.c[i] >= WATHCHDOG_LIMIT);
  }
}

void showTimerState()
{
  for(int i = 0; i < 4; i++)
  {
    digitalWrite(i+LED_A, gLkTmr > i ? LOW : HIGH);
  }
}

void showLockState()
{
  for(int i = 0; i < 4; i++)
  {
    digitalWrite(i+LED_A, gLockLed.s[i]);
  }
}

void debugBtnShow(unsigned int set)
{
  readBtn(set);
  gLockLed = gBtn;
  showLockState();
}

void triggerLock()
{
  for(int i = 0; i < 4; i++)
  {
#ifdef ACTIVE_LOW_RELAY
    digitalWrite(i+LCK_A, !(gLock.s[i] && !gWatchDogHit.s[i]));
#else
    digitalWrite(i+LCK_A, (gLock.s[i] && !gWatchDogHit.s[i]));
#endif
  }
}

void readBtn(unsigned int set)
{
  //disable all sets and reset state
  for(int i = 0; i < 4; i++)
  {
    digitalWrite(B_EN_A+i, 0);
    gBtn.s[i] = false;
  }

  //if valid set, read in buttons
  if(set < 4)
  {
    digitalWrite(B_EN_A+set, 1);
    for(int i = 0; i < 4; i++) { gBtn.s[i] = analogRead(i+B_IN_A) > 111; }
  }
}

void toggleTimer()
{
  gLkTmr = (gLkTmr + 4) % 5;
}

void enableTimer(bool en)
{
  if(en)
  {
    gLkTmr = 4;
  }
  else
  {
    gLkTmr = 0;
  }
}

void setAllState(bool takenState)
{
  for(int i = 0; i < 4; i++)
  {
    gLockLed.s[i] = takenState;
  }
}

void hrHit()
{
  gHrTmr = LOOPS_TO_HR;

  if(gLkTmr)
  {
    gLkTmr--;
    if(!gLkTmr)
    {
      setAllState(TAKEN);
    }
  }
}